## Slide 1
MAV Manager
(mav_manger)
Provides a high level interface to manage the system. Primarily communicates with the trackers manager, but can specify position and velocity goals as well as trigger transitions between trackers.
State Estimator
(vicon_odom or your own)
This leverages Vicon, Qualisys, or can use your own state estimator. In particular, this publishes a nav_msgs/Odometry message, which contains the position, pose, linear velocity, angular velocity, etc.
SO3-based Control
(so3_control)
Computes a desired orientation and thrust for the robot.
Trackers Manager
(trackers/trackers_manager)
Manages and switches between trackers such as line trackers, velocity trackers, etc. Each tracker is responsible for sending a command that specifies a desired position, velocity, acceleration, yaw, and yaw_dot. The message also includes gains, etc.
quadrotor_simulator
PX4 SITL
snavquad_interface
mavros_interface
crazyflie_interface
User
Rviz
(waypoint_navigation_tool)
Motors On/Off
Takeoff/Land
GoTo Waypoint
(rqt_mav_manager)
Trajectory Generator
Compute a trajectory from multiple waypoints
yourown_interface
Waypoints
Snapdragon Flight
Crazyflie
Your Own Quad
Gazebo
PX4
FLA
Gazebo
odom
snav_vio_odom
yourown_odom
so3_command / trpy command
ground_truth_odom
ros_package_name
Simulation

## Slide 2
MAV Manager (optional)
Provides a high level interface to manage the system. Primarily communicates with the trackers manager, but can specify position and velocity goals as well as trigger transitions between trackers.
Quad Encode Message
(quad_encode_msg)
Encodes messages for serial transfer to the robot. Such commands can be desired attitudes, thrust, PWM signals, etc.
Quad Decode Message
(quad_decode_msg)
Decodes serial messages from the robot. Messages contain IMU, pressure sensor, battery voltage, etc.
State Estimator
(vicon_odom or your own)
This leverages Vicon, Qualisys, or can use your own state estimator. In particular, this publishes a nav_msgs/Odometry message, which contains the position, pose, linear velocity, angular velocity, etc.
Robot
Can be simulated using quadrotor simulator.
PositionCommand
SO3Command
Quad Serial Comm
(quad_serial_comm)
Sends/receives serial messages to/from the robot
Quadrotor Simulator
(quadrotor_simulator)
OutputData
Always Needed
Needed for Simulation
Needed for Real Flights with Hummingbird
SO3-based Control
(so3_control)
Computes a desired orientation and thrust for the robot.
Trackers Manager
(trackers/trackers_manager)
Manages and switches between trackers such as line trackers, velocity trackers, etc. Each tracker is responsible for sending a command that specifies a desired position, velocity, acceleration, yaw, and yaw_dot. The message also includes gains, etc.